## Slide 1: Automated Wire Cutting and Stripping Machine
Group No : 48
IN 1900 ( ICT Project)
Final Presentation

## Slide 2: Group Members
Name | Reg. No: | Photo
Wanni Arachchi H.N. | 204226H | 
Thiunuwan G.V.R. | 204219N | 
Avishka W.D. | 204012A | 
Kavindi G.V.M. | 204099T | 
Hemarathna H.A.T.N. | 204072F | 

## Slide 3: Problem in brief
When customer needs wires of different sizes, they have to re-measure the length of wires every time.
It leads to waste of the time.
There must be a person always to cut and strip wires manually.
The wires can be intertwined when winding manually.
There are some situations that we need to strip large multicore and large gauged cables. It is difficult to
strip wires manually.
It is hard to cut and strip large sizes and large number of wires.

## Slide 4: Project Aim & Objectives
Aim:
This project aim to design and develop an Automated Wire Cutting and Stripping Machine.
Objectives:
To cut wires automatically according to the different measurements given by the user.
To wind the wires automatically instead of using manual winding process.
To strip wires automatically instead of using manual stripping process.
To reduce waste of time and labor by automating the manual wire cutting process.

## Slide 5: Proposed Solution
Infrared Sensor
Keypad
Ultrasonic sensor x 3
User Inputs (Length, Quantity)
Distance to wire
1.Distance
2.Distance to Pallet
3.Ditect the position of
cutting wheel
Servo Motor
(Hold the wire)
DC Motor
(Cut the wire)
Stepper Motor
1.Measure the length
2.Wrap the wire
3.Rotation wheel
4.Move the wire
5.Adjust blade’s position
6..Adjust blade’s height
Display
Buzzer
Length Quantity
Rotate Motor
Rotate Motor
Rotate Motor
Beep Sound
Inputs
Outputs
Microcontroller

## Slide 6: Circuit Diagram

## Slide 7: Google Document for 3D Diagram: https://drive.google.com/file/d/1Kw-JoECkxSk__5hSdx6c1PA0WzxhlRKf/view?usp=sharing
3D Diagram

## Slide 9: Process of Stripping Part
h1
Initial position of the moving pallet
h1 - Initial distance between moving
pallet and ultrasonic sensor
h1 - d
d-Diameter of the wire the

## Slide 10
h2
h3
Plate B
h2 - Distance between ultrasonic sensor and plate B
h3 - Distance between the surface of box and cutting blade
h2 = h3 (we adjust like this for get simplified equations at next steps)
box
Initial position of the cutting blade
h3

## Slide 11
x- depth
d
x
Position of the blade after horizontal and vertical movements
d-x
h3-(d-x) = The distance that cutting blade should move vertically
For that the whole unit (cutting part) should move downwards until the reading equals to h2+h3-(d-x).

## Slide 12: Resource Required
Software:
Microchip Studio.
Blender.
SimulIDE.
Proteus.
Hardware:
Sensors: Infrared Sensor x 3 .
Ultrasonic Sensor x 3 .
Microcontroller: Atmega32 x 2.
Servo Motor x 1.
DC Motor x 1 .
Stepper Motor x 6.
16x2 LCD Display x 1.
Buzzer x 1.
4x4 Keypad x 1.
Stepper Motor Drivers(ULN2803) x 6.
DC Motor Driver(L293D) x 1.
Relay x 3

## Slide 13: Cost Estimation
Table 1: Cost Estimation [1]
Item Name | Quantity | Unit Price | Cost
Keypad | 1 | 160 LKR | 160 LKR
Ultrasonic Sensor | 3 | 410 LKR | 1230 LKR
Infrared Sensor | 3 | 150 LKR | 450 LKR
Servo Motor | 1 | 600 LKR | 600 LKR
Stepper Motor | 7 | 1750 LKR | 12250 LKR
Stepper Motor Driver (ULN 2003) | 7 | 340 LKR | 2380 LKR
DC Motor Driver (L293D) | 1 | 540 LKR | 540 LKR
Atmega 32 Microcontroller | 2 | 550 LKR | 1100 LKR
LCD Display (16x2) | 1 | 950 LKR | 950 LKR
Buzzer | 1 | 100 LKR | 100 LKR
DC Motor | 1 | 1250 LKR | 1,200 LKR
Timing Pulley | 1 | 1000 LKR | 1000 LKR
Power Supply Unit | 1 | 2000 LKR | 2000 LKR
1 Channel Relay | 3 | 200 LKR | 600 LKR
Other |  |  | 
Total Cost |  |  | 24560 LKR

## Slide 14: Individual contribution Member 1: Avishka W.D (204012A)
Contributed to the Blender animation
Responsible Components : 1). Ultra Sonic Sensor
2). 2 Stepper Motors
h1
Initial position of the moving pallet
h1 - Initial distance between moving
pallet and ultrasonic sensor
h1 - d
d-Diameter of the wire the

## Slide 15
1). Stepper Motor
A+ pin B+ pin Common A- pin B- pin
Pin Diagram
Circuit Diagram
Stepper Motor
Link for Stepper Motor Datasheet:
https://components101.com/sites/default/files/component_datasheet/NEMA23%20Stepper%20Motor.pdf
Rated Voltage: 3.2V
Rated current: 2.8A
Step Angle : 1.8 degree
200 steps per revolution
Weight (Kg) 1.05
Holding Torque (N.cm) :189

## Slide 16
Code for Stepper Motor

## Slide 17
2). Ultrasonic Sensor
Pin Diagram
Circuit Diagram
Link for Ultrasonic Sensor Datasheet:
https://www.mouser.com/datasheet/2/813/HCSR04-2307007.pdf
Working Voltage: DC 5 V
Working current: 15mA
Working Frequency 40Hz
Ranging Distance : 2cm – 400cm/4m
Dimension: 45mm x 20mm x 15mm

## Slide 18
Code for Ultrasonic Sensor

## Slide 19: Member 2: H.A.T.N.Hemarathna (204072F)
Responsible Components : 1).16 x 2 LCD Display
2). 4 x 4 Keypad
3). Buzzer
3D diagram

## Slide 20: 1). 16 x 2 LCD Display
Voltage Supply Pins
Control Pins
Data Pins
Operating voltage : 4.8-5.3V
Maximum Current Range:1.5-2.3mA
Working temperature: 0-50°C
Circuit Diagrams for LCD and Keypad
LCD 5x7 dot matrix
VSS= Ground pin
VDD= Supply Voltage
VEE= Contrast control pin
RS= Register Select
RW= Read/ Write
E= Enable
D0-D7= Data pins
Inputs
1.Cutting mode or Stripping
mode
Cutting Mode
2.Length of a piece
If length<50
3.No of pieces
Stripping Mode
4.Strip Height
5.Strip Length

## Slide 21
2). 4x4 Keypad
Link for 4x4 Keypad Datasheet:
https://components101.com/sites/default/files/component_datasheet/4x4%20Keypad%20Module%20Datasheet.pdf
Link for LCD Datasheet:
https://components101.com/displays/16x2-lcd-pinout-datasheet
Maximum Voltage across each button :24V
Maximum Current through each button:30mA
Maximum operating temperature: 0°C to + 50°C
1 1 1 1
Col1 Col2 Col3 Col4
(PA4) (PA5) (PA6) (PA7)
(Columns)
Keypad Sensor
Keypad Pin Diagram
Internal Circuit Diagram
0 Row1-(PA0)
0 Row2-(PA1)
0 Row3-(PA2)
0 Row4-(PA3)
(Rows)

## Slide 22: Circuit for LCD Display and Keypad

## Slide 23: 1). LCD header file
Code

## Slide 24: 2). LCD c file

## Slide 25: 3). Keypad header file

## Slide 26: 4). Keypad c file

## Slide 27
5). Main Code for LCD Display and Keypad

## Slide 30
03). Buzzer
(+) Terminal or Positive pin is connected to VCC
(-) Terminal or Negative pin is connected to Ground
Operating voltage :3 to 30V DC
Rated current: 30mA
Operating temperature : -20 to +60ºC
Link for Buzzer Datasheet:
https://www.farnell.com/datasheets/1662133.pdf
Piezo Buzzer Pin Diagram
Buzzer Vibration

## Slide 31: Buzzer Circuit Diagram
Buzzer Circuit Diagram

## Slide 32
Buzzer header file
Buzzer c file

## Slide 33
Stepper motor
servo motor
IR sensor.
Member 3: Kavindi G.V.M (204099T)

## Slide 34
01). IR Sensor
OUT = Active High Output
GND = Power Supply Ground
Vcc = Power Supply Input
TestPin = Test Pin
Link for IR Sensor Datasheet:
https://components101.com/sites/default/files/component_datasheet/Datasheet%20of%20IR%20%20Sensor.pdf
Operating Voltage: 5V
Size: 50 x 20 x 10 mm (L x B x H)
5VDC operating voltage.
20mA supply current.
I/O pins are 5V and 3.3V compliant.
Adjustable Sensing range.
IR sensor
Circuit Diagram
Pin Diagram
33434343434343

## Slide 35
Code for IR Sensor
34

## Slide 36
02). Stepper Motor
Maximum Voltage:2.8V
Maximum current:1.68A
Weight : 1.05 kg
Temperature Rise ( `c):80 Max (rated current 2 phase on)
A+ pin B+ pin Common A- pin B- pin
Circuit Diagram
Link for Stepper Motor Datasheet:
https://components101.com/sites/default/files/component_datasheet/NEMA23%20Stepper%20Motor.pdf
Stepper Motor
Stepper Motor
Pin Diagram
35

## Slide 37
C file Code for Stepper Motor

## Slide 38
h File Code for Stepper Motor

## Slide 39
03). Servo Motor
V+ =VCC pin
Gnd =Ground pin
Sg =PWM Signal pin
Maximum Voltage : 6.0V
Maximum Current : 100mA
Speed: 4.8V: 0.10 sec/60°
Motor Type: 3-pole
Rotational Range: 180°
Link for Servo Motor Datasheet:
https://datasheetspdf.com/pdf-file/791970/TowerPro/SG90/1
Circuit Diagram
Pin Diagram
Servo Motor
39

## Slide 40
C File Code for Servo Motor

## Slide 41
H File Code for Servo Motor

## Slide 42: Member 4:Thiunuwan G.V.R (204219N)
Responsible Components : 1).Stepper Motor (x2)
2).Ultrasonic Sensor
3).DC Motor
Contributed to making Animation For the project..
DC Motor
Stepper Motor(M3)
Stepper Motor(M2)
Ultrasonic Sensor(B)

## Slide 43
01). Stepper Motor
Rated Voltage: 3.2V
Rated current: 2.8A
Step Angle : 1.8 degree
200 steps per revolution
Weight (Kg) 1.05
Holding Torque (N.cm) :189
Link for Stepper Motor Datasheet:
https://components101.com/sites/default/files/component_datasheet/NEMA23%20Stepper%20Motor.pdf
Link for Stepper Motor Driver Datasheet:
https://www.mouser.com/datasheet/2/389/cd00000179-1795140.pdf
Stepper Motor
Pin Diagram (Stepper Motor)
Input pins
Output pins
Pin Diagram(Stepper Motor Driver)
Common pin

## Slide 44
Stepper Motor(M3) Code
C file for the StepperM3 code
Header file for the StepperM3 code

## Slide 45
Circuit Diagram for Stepper Motor (M3)

## Slide 46
Pin Diagram
02). Ultrasonic Sensor
Link for Ultrasonic Sensor Datasheet:
https://www.mouser.com/datasheet/2/813/HCSR04-2307007.pdf
Working Voltage: DC 5 V
Working current: 15mA
Working Frequency 40Hz
Ranging Distance : 2cm – 400cm/4m
Dimension: 45mm x 20mm x 15mm
Trigger pin
Echo pin
Ground pin
VCC pin
Distance = Time × Velocity of sound / 2
Velocity of Sound- 340 m/s

## Slide 47
h2
h3
Plate B
h2 - Distance between ultrasonic sensor and plate B
h3 - Distance between the surface of box and cutting blade
box
Initial position of the cutting blade
h3

## Slide 48
x- depth
d
x
Position of the blade after horizontal and vertical movements
d-x
h3-(d-x) = The distance that cutting blade should move vertically
For that the whole unit (cutting part) should move downwards until the reading equals to h3-(d-x)+h2.

## Slide 49
Ultrasonic Sensor And Stepper (M2) Code
Header file for the Ultrasonic sensor code
C file for the Ultrasonic sensor code

## Slide 50
C file for the Stepper(M2) code
Header file for the Stepper(M2) code

## Slide 51
Circuit Diagram for Ultrasonic(B) and Stepper (M2)

## Slide 52
03). DC Motor
Input Voltage : 18.0 V
No Load Current : 3.90 A
Maximum current : 93.98 A
No-load rpm : 22500 rpm
Speed at Maximum Efficiency : 19500 rpm
Maximum torque is 1.4Nm (1400mNm)
Maximum Output Power : 830.00 W
Model:HC877P-011
Weight : 464 g
Link for DC Motor Datasheet:
https://drive.google.com/file/d/17K9uFVYDhlmqAupovslFl-kK8AhKpcPC/view?usp=sharing
Link for DC Motor Driver (L293D) Datasheet:
https://www.mouser.com/datasheet/2/389/cd00000059-1795435.pdf
+pin
-pin
Pin Diagram (DC Motor)
Ground pin
Output pins
(motor1)
Output pins
(motor2)
Input pins
(motor1)
Input pins
(motor2)
Voltage supply pins
Pin Diagram (DC Motor Driver)

## Slide 53
Code for DC Motor
C file for the for-DC Motor code
DC Motor Code

## Slide 54
Circuit Diagram for DC Motor
Header file for the DC Motor code

## Slide 55
Member 1:Wanni Arachchi H.N (204226H)
Responsible Components : 1).Stepper Motor (x2)
2).Ultrasonic Sensor
3).IR Sensor(x2)
Making power supply unit
IR sensor1
Stepper Motor 2
IR sensor2
Stepper Motor 1

## Slide 56
Link for IR Sensor Datasheet:
https://components101.com/sites/default/files/component_datasheet/Datasheet%20of%20IR%20%20Sensor.pdf
OUT = Active High Output
GND = Ground
Vcc = Power Supply Input
01) .IR Sensor
Pin Diagram
Operating Voltage | 3.3V – 5V
Operating Current | 15 mA
Comparator chip | LM393
Sensor type | YG1006 Photo Transistor
Sensitivity | Adjustable via potentiometer
Output type | Digital output / Digital and Analog output
LED lights indicators | Power (red) and Output (green)
Spectrum range | 760nm ~ 1100nm
Detection angle | 0 – 60 degree
Operating temperature | -25℃ ~ 85℃
PCB Size | 3cm X 1.6cm
Internal circuit diagram

## Slide 57
Circuit diagram for IR sensor 1 and IR sensor 2

## Slide 58
IR sensor 01- C file
IR sensor 01- header file

## Slide 59
IR sensor 02- C file
IR sensor 02- header file

## Slide 60
Step angle of the motor : 1.8 deg.
Steps for one circle : 200
The pully design as when the stepper motor finished one step the belt moves 1mm.
When small driving pully finished one round belt move forward 20cm (0.1x200)
When stepper motor finished one round the wire go forward 20cm

## Slide 61
A+ pin B+ pin Common A- pin B- pin
Pin Diagram
02). Stepper Motor 01
Link for Stepper Motor Datasheet:
https://components101.com/motors/nema17-stepper-motor
NEMA 17 Stepper Motor Technical Specifications
Rated Voltage: 12V DC
Current: 1.2A at 4V
Step Angle: 1.8 deg.
No. of Phases: 4
Motor Length: 1.54 inches
4-wire, 8-inch lead
200 steps per revolution, 1.8 degrees
Operating Temperature: -10 to 40 °C
Unipolar Holding Torque: 22.2 oz-in

## Slide 62
Circuit diagram for Stepper motor 1
Header file for Stepper motor 1

## Slide 63
C Code for Stepper Motor
Process of Stepper Motor

## Slide 64
Link for Ultrasonic sensor Datasheet:
https://www.mouser.in/datasheet/2/813/HCSR04-2307007.pdf
03). Ultrasonic Sensor
Pin Diagram
Specifications
Power Supply: DC 5V
Working Current: 15mA
Working Frequency: 40Hz
Ranging Distance : 2cm – 400cm/4m
Resolution : 0.3 cm
Measuring Angle: 15 degree
Trigger Input Pulse width: 10uS
Dimension: 45mm x 20mm x 15mm

## Slide 65
H1
Circuit diagram for ultrasonic sensor and stepper 02

## Slide 66
Header file for stepper 02
C file for stepper 02

## Slide 67
Header file for ultrasonic sensor

## Slide 68
C file for ultrasonic sensor

## Slide 72
Circuit diagram for power supply

## Slide 73
References
[1]"Products - TRONIC.LK", Tronic.lk, 2021. [Online]. Available: https://tronic.lk/shop/products.
"ElectronicWings - Hardware Developers Community", Electronicwings.com, 2021. [Online]. Available: https://www.electronicwings.com/.
"What's going on?", AVR Freaks, 2021. [Online]. Available: https://www.avrfreaks.net/.
https://www.youtube.com/redirect?event=video_description&redir_token=QUFFLUhqbTJxRE5kU09QQ3dNTkQ5RmExLWVDSll2dFRFZ3xBQ3Jtc0tuZDFYZy1aUUpkcGxHQndHUTlrdHpaem15QThma2VhbFVCZVFpZ0g5RlhuNl9TZXNFNU5IZ0kzMDRYbzhscUFlTGNxeDBjWUFRYkNweFFnaUg1MTZ2ajk1SUg1ZVlvbDdjcFZrR0Nta3o1NnltRUEwRQ&q=http%3A%2F%2Fwww.engineeringfunda.co.in

## Slide 74
Thank You!
Questions?